## Slide 1
RISC-V
RV32I 설계
발표자 | 최기훈
2026.05.26

## Slide 2
목차
01 | 개요 및 목표
02 | Design B/D
03 | TYPE 별 설명
04 | 1to10 adder
05 | Trouble shooting
06 | 고찰

## Slide 3
개요 및 목적
RISC (Reduced Instruction Set Computer) 구조
-기존의 CISC 보다 적은 수의 명령어
-여러 타입의 명령어를 통한 CPU 제어
-회로 구성이 단순하며 기본적으로 32bit 명령어를 사용
1.SystemVerilog를 이용한 RV32I CPU 구현
-ALU,MEM,PC 등 여러 모듈을 구현
-RAM/ROM 메모리 구조 이해 및 활용
-RISC-V 명령어의 이해 및 활용
2.RISC-V 구조 활용
각 타입 명령어 및 동작의 이해
C 언어 동작을 RISC-V를 통해 구현

## Slide 4
Design B/D
전체 회로도
CPU 회로

## Slide 5
TYPE별 설명 (R-TYPE)

## Slide 6
TYPE별 설명 (R-TYPE)
SUB,SRA

## Slide 7
TYPE별 설명 (R-TYPE)
PC | Instruction | rs1 | rs2 | rd | Result
0 | add x5,x1,x2 | 1 | 2 | 5 | x5=3
4 | sub x6,x2,x1 | 2 | 1 | 6 | x6=1
8 | and x7,x3,x1 | 3 | 1 | 7 | x7=1
12 | or x8,x3,x1 | 3 | 1 | 8 | x8=3
16 | xor x9,x3,x1 | 3 | 1 | 9 | x9=2
20 | sll x10,x1,x2 | 1 | 2 | 10 | x10=4
24 | srl x11,x8,x1 | 8 | 1 | 11 | x11=4
28 | sra x12,x13,x1 | 13 | 1 | 12 | x12=-2147483642
32 | slt x13,x1,x2 | 1 | 2 | 13 | x13=1
36 | sltu x14,x1,x2 | 1 | 2 | 14 | x14=1

## Slide 8
TYPE별 설명 (R-TYPE)
x5(ADD) = 1 + 2 = 3
X6(SUB) = 3 - 3 = 0
X7(AND) = 7(111) & 3(011) = 3(011)
X8(OR) = 8(1000) | 3(011) = 11(1011)
x9(XOR) = 9(1001) ^ 3(011) = 10(1010)
X10(SLL) = 11 << 31 = -214783648
X11(SRL) = 10(1010) >> 30 = 0
X12(SRA) = x10 >> 12 = -2
X13(SLT) = 3 < 4 = 1
X14(SLTU) = 4 < 3 = 0
※Signed

## Slide 9
TYPE별 설명 (I-TYPE)

## Slide 10
TYPE별 설명 (I-TYPE)
ALU Function Control [Imm]
Shift Register (SLLI, SRLI, SRAI)

## Slide 11
TYPE별 설명 (I-TYPE)
IMM값
PC | Instr | 계산 | 결과
4 | addi x5,x1,-1 | 1 + (-1) | x5 = 0
8 | andi x6,x2,15 | 2 & 15 | x6 = 2
12 | ori x7,x2,15 | 2 ¦ 15 | x7 = 15
16 | xori x8,x8,255 | 8 ^ 255 | x8 = 247
20 | slti x9,x3,5 | 3 < 5 | x9 = 1
24 | slli x10,x1,31 | 1 << 31 | x10 = 0x80000000
28 | srli x11,x10,30 | 0x80000000 >> 30 | x11 = 0x00000002
32 | srai x12,x10,30 | arithmetic shift | x12 = 0xFFFFFFFE

## Slide 12
TYPE별 설명 (I-TYPE)
X5(ADDI) = 1 + (-1) =0
X6(ANDI) = 2 & 15 = 2
X7(ORI) = 2 | 15 = 15
X8(XORI) = 8 ^ 255 =247
X9(SLTI) = 3 < 5 = 1
X10(SLLI) = 1 << 31 = -2147483648
X11(SRLI) = X10 >> 30 = 2
X12(SRAI) = X10 >> 30 = -2

## Slide 13
TYPE별 설명 (S-TYPE)

## Slide 14
TYPE별 설명 (S-TYPE)
Store data into RAM

## Slide 15
TYPE별 설명 (L-TYPE)
rd = M[rs1 + imm]

## Slide 16
TYPE별 설명 (L-TYPE)

## Slide 17
TYPE별 설명 (S-TYPE & L-TYPE)
PC | Instruction | 동작 | 결과
0 | addi x3,x0,16 | base 주소 설정 | x3=0x10
1 | addi x11,x0,-1 | -1 생성 | x11=FFFFFFFF
2 | lui x12,0x10 | upper 생성 | x12=00010000
3 | addi x12,x12,-1 | 하위값 조정 | x12=0000FFFF
4 | sb x11,0(x3) | byte 저장 | MEM[0x10]=FF
5 | sh x12,4(x3) | half 저장 | MEM[0x14]=FFFF
6 | sw x11,8(x3) | word 저장 | MEM[0x18]=FFFFFFFF
7 | lb x8,0(x3) | signed byte load | x8=FFFFFFFF
8 | lbu x9,0(x3) | unsigned byte load | x9=000000FF
9 | lh x10,4(x3) | signed half load | x10=FFFFFFFF
10 | lhu x11,4(x3) | unsigned half load | x11=0000FFFF
11 | lw x12,8(x3) | word load | x12=FFFFFFFF

## Slide 18
TYPE별 설명 (S-TYPE & L-TYPE)
PC | Instruction | 동작 | 결과
0 | addi x3,x0,16 | base 주소 설정 | x3=0x10
1 | addi x11,x0,-1 | -1 생성 | x11=FFFFFFFF
2 | lui x12,0x10 | upper 생성 | x12=00010000
3 | addi x12,x12,-1 | 하위값 조정 | x12=0000FFFF
4 | sb x11,0(x3) | byte 저장 | MEM[0x10]=FF
5 | sh x12,4(x3) | half 저장 | MEM[0x14]=FFFF
6 | sw x11,8(x3) | word 저장 | MEM[0x18]=FFFFFFFF
7 | lb x8,0(x3) | signed byte load | x8=FFFFFFFF
8 | lbu x9,0(x3) | unsigned byte load | x9=000000FF
9 | lh x10,4(x3) | signed half load | x10=FFFFFFFF
10 | lhu x11,4(x3) | unsigned half load | x11=0000FFFF
11 | lw x12,8(x3) | word load | x12=FFFFFFFF

## Slide 19
TYPE별 설명(B-TYPE)
rs1

## Slide 20
TYPE별 설명(B-TYPE)
rs1
Compare Data & Make Branch ( PC += Imm)

## Slide 21
TYPE별 설명(B-TYPE)
PC | Instruction | Condition | Branch | Next PC
0 | beq x1,x1 | 1 == 1 | taken | 8
8 | beq x1,x2 | 1 == 2 | not taken | 12
12 | bne x1,x2 | 1 != 2 | taken | 20
20 | bne x1,x1 | 1 != 1 | not taken | 24
24 | blt x1,x2 | 1 < 2 | taken | 32
32 | blt x2,x1 | 2 < 1 | not taken | 36
36 | bge x2,x1 | 2 >= 1 | taken | 44
44 | bge x1,x2 | 1 >= 2 | not taken | 48
48 | bltu x1,x2 | 1 < 2 | taken | 56
56 | bltu x2,x1 | 2 < 1 | not taken | 60
60 | bgeu x2,x1 | 2 >= 1 | taken | 68
68 | bgeu x1,x2 | 1 >= 2 | not taken | 72

## Slide 22
TYPE별 설명(B-TYPE)
PC | Instruction | Condition | Branch | Next PC
0 | beq x1,x1 | 1 == 1 | taken | 8
8 | beq x1,x2 | 1 == 2 | not taken | 12
12 | bne x1,x2 | 1 != 2 | taken | 20
20 | bne x1,x1 | 1 != 1 | not taken | 24
24 | blt x1,x2 | 1 < 2 | taken | 32
32 | blt x2,x1 | 2 < 1 | not taken | 36
36 | bge x2,x1 | 2 >= 1 | taken | 44
44 | bge x1,x2 | 1 >= 2 | not taken | 48
48 | bltu x1,x2 | 1 < 2 | taken | 56
56 | bltu x2,x1 | 2 < 1 | not taken | 60
60 | bgeu x2,x1 | 2 >= 1 | taken | 68
68 | bgeu x1,x2 | 1 >= 2 | not taken | 72

## Slide 23
TYPE별 설명(UL-TYPE)

## Slide 24
TYPE별 설명(UA-TYPE)

## Slide 25
TYPE별 설명(UL-TYPE & UA-TYPE)
PC | Instr | Type | Operation | Result
0 | lui x5,0x12345 | LUI | x5 = 0x12345000 | x5 = 0x12345000
4 | auipc x6,0x1 | AUIPC | x6 = PC + 0x1000 | x6 = 0x00001004
Address Shift / Jump (imm << 12)
Address Shift / Jump PC + (imm << 12)
LUI
AUIPC

## Slide 26
TYPE별 설명(UL-TYPE & UA-TYPE)
PC | Instr | Type | Operation | Result
0 | lui x5,0x12345 | LUI | x5 = 0x12345000 | x5 = 0x12345000
4 | auipc x6,0x1 | AUIPC | x6 = PC + 0x1000 | x6 = 0x00001004

## Slide 27
TYPE별 설명 (J-TYPE)
rd = PC + 4
PC += imm

## Slide 28
TYPE별 설명 (J-TYPE)
rd = PC + 4
PC += imm
Address Shift / Jump + Read (인터럽트에 활용)
RD = PC +4 ;
PC += imm ;

## Slide 29
TYPE별 설명 (JL-TYPE)
rd = PC + 4
PC += rs1 + imm

## Slide 30
TYPE별 설명 (JL-TYPE)
Address Shift / Jump + Read (인터럽트에 활용)
RD = PC +4 ;
PC = RS1 + imm ;
rd = PC + 4
PC += rs1 + imm

## Slide 31
TYPE별 설명 (J-TYPE & JL-TYPE)
PC | Instr | Type | rd | wb_out | PC next | 설명
0 | jal x1,+8 | JAL | x1 | 4 | 8 | jump
8 | nop | - | - | - | 12 | Nop
12 | nop | - | - | - | 16 | nop
16 | jalr x2,0(x4) | JALR | x4 | 20 | 4 | return

## Slide 32
TYPE별 설명 (J-TYPE & JL-TYPE)
PC | Instr | Type | rd | wb_out | PC next | 설명
0 | jal x1,+8 | JAL | x1 | 4 | 8 | jump
8 | nop | - | - | - | 12 | Nop
12 | nop | - | - | - | 16 | nop
16 | jalr x2,0(x4) | JALR | x4 | 20 | 4 | return

## Slide 33
1to10 adder

## Slide 34
1to10 adder
SCOPE

## Slide 35
1to10 adder
A4=<a5 라면

## Slide 36
1to10 adder
(S0-20)/4 = 59
(S0-24)/4 = 58
Adder 함수 시작

## Slide 37
1to10 adder
Sp = 192
220(55)
216(54)
Sp+32

## Slide 38
1to10 adder
+
220(55)
216(54)
256
224
pc_next = ra

## Slide 39
1to10 adder
현재 s0 = 256
(S0-24)/4 =58
(S0-20)/4 =59

## Slide 40
1to10 adder
a4=<a5 일때까지 반복

## Slide 41
1to10 adder
LUI의 Imm은 20bit만
가능하기 때문

## Slide 42
Trouble shooting
B타입 동작일때 rs1 이나 rs2 가 x 값이라면 비교할 때 b_taken이 x가 출력되는 문제가 발생

## Slide 43
Trouble shooting
b_taken 출력을 If문을 사용하여 출력하도록 변경

## Slide 44
Trouble shooting

## Slide 45
고찰
RV32I를 구현하면서 BEQ 같은 분기 명령이 단순 비교가 아니라 PC 변경과 연결된다는 점을 이해하게 되었고, 데이터 흐름 전체를 고려해야 정상 동작한다는 것을 알게 되었다.
C 언어로 작성된 코드를 RV32I 구조로 변환하는 과정에서 한 줄의 코드도 여러 하드웨어 동작(레지스터 읽기, ALU 연산, 메모리 접근)으로 나뉜다는 점을 체감했다.
전체 설계에서 작은 문법 오류보다도 구조(데이터 흐름, 신호 연결)를 제대로 잡는 것이 더 중요하다는 것을 느꼈다.